COMPARISON OF PERFORMANCES OF LOW TEMPERATURE RADIANT HEATING SYSTEMS

Dragan Cvetković*, Marko Miletić, Jasmina Skerlić, Danijela Nikolić, Milorad Bojić,

Faculty of Engineering Sciences of Kragujevac University, Sestre Janjić 6, 34 000 Kragujevac, Serbia

* Dragan Cvetković, e-mail:dragan_cw8202@yahoo.com, tel. 034-330196

Abstract: Low temperature heating panel systems offer distinctive advantages in terms of thermal comfort and energy consumption, allowing work with low exergy sources. The purpose of this paper is to compare floor, wall, ceiling, and floor-ceiling panel heating systems in terms of energy, exergy and CO2 emissions. The operation of each of these low-temperature systems is simulated in the same building - a residential house for one family. Simulation models are developed by using EnergyPlus software developed by Lawrence Berkeley Laboratory in the United States.

Key words: Low temperature heating, wall heating, floor heating, ceiling heating, Energy Plus

- Introduction

In Europe, today are increasingly using low-temperature panel heating and cooling systems for residential buildings, according to some studies, this figure exceeds 50% [1,2]. Saving energy with panel system according to some studies more than 30% [3,4].

Low temperature radiant systems are very complex because they involve different mechanisms of heat transfer, conduction through the walls, convection between the building surface and indoor air, radiation between the panel and surrounding areas and the conduction between the floor area and ground. The main essence of the low-temperature air systems is to provide adequate thermal comfort at significantly lower temperatures and to prevent overheating of the rooms in heating mode.

A large number of studies devoted to laboratory tests of panel systems in terms of heat transfer research and development of new management methods [5-10]. However, in terms of modeling, there are several analytical studies on the thermal characteristics of the panel system. The earliest model Lises and Kollmar [11] showed that heat loss is mainly from the upper surface of the board. Leal and Miller [12] have used analytical and numerical methods for determining the temperature in heating pavement. Zhang and Pate have developed a two-dimensional finite element method for the ceiling panel heating, which is used to model the heating low-temperature heating systems[13,14]. Kilkis [15] developed the so-called stationary composite model for modeling of radiant systems for heating and cooling. After that, Kilkis and Sapci [16] and Kilkis and Coley [17] have used this model and develop software for the design of floor heating and cooling systems.

Maloney [18] developed a model for radiant heating panels for BLAST software. Strand and Pedersen [19,20] used the method of transfer by conduction and developed a model for radiant heating and cooling within the EnergyPlus. Miriel [21] is used TRNSYS software for modeling the ceiling panels for heating and cooling. Abdelaziz Laouadi [22] developed one-dimensional numerical software with two-dimensional analytical model of floor/ceiling heating systems, which compared to earlier works, based on one-dimensional numerical models, provides better prediction of the temperature between the concrete and pipes, which leads to more accurate calculation of other necessary parameters (thermal comfort, capacity boilers, heating control, the minimum and maximum floor temperature). So far, no published papers are found devoted to the comparison of higher number of the panel heating systems from different points of view: energy, exergy, and environmental protection.

This paper presents research with an objective to compare the heating effects of several panel heating systems: floor, wall, ceiling, and floor-ceiling. These low-temperature heating systems are simulated for the same residential house by using simulation models of EnergyPlus. The obtained parameters of energy and exergy consumption and that of CO2 emission are mutually compared for the simulated cases and different conclusions are obtained.

- Building description

The analyzed building is a residential family house shown in Figure 1. Itsarchitecture has evolved from research within the project "Research and development of Serbian homes zero net-energy consumption" financed by the Ministry of Science of Serbia. The building is designed for one family and has a living area of 190.08 m2. The envelope of the building is made ​​of 190mm porous brick , 50mm thermal insulating layer  and 20mm lime mortar. The U-value is 0,57W/(m2K). The windows are double glazed with U-value of 2.72 W/(m2K). The overall ratio of glass to the exterior walls is 7.32%, where the total area of exterior walls is 264.35m2 and area of windows 19.36m2.

Figure 1. Analyzed building

- Location and climate

The analyzed building is located in Kragujevac, Serbia. Elevation of Kragujevac is 209m, and its latitude and longitude are 44o1N and 20o55E. The city has a continental temperate climate with four different seasons (summer, autumn, winter, and spring). As part of the EnergyPlus, weather file used as an epw file generated by the Meteonorm [23]. Heating season runs in the Kragujevac from 15October to 15April [24].

Table 1.Monthly averages for Kragujevac, Serbia [25]

| Month | Mean Temperature °C | Average Precipitation (mm) | Mean Number of Precipitation Days |
| --- | --- | --- | --- |
|  | Daily Minimum | Daily Maximum |  |  |
| Jan | -3.8 | 3.8 | 4.1 | 11.6 |
| Feb | -1.7 | 6.7 | 3.87 | 10.4 |
| Mar | 1.4 | 11.8 | 4.44 | 10.6 |
| Apr | 5.5 | 17.3 | 4.94 | 12.2 |
| May | 10.1 | 22.0 | 7.38 | 13.1 |
| Jun | 13.0 | 25.0 | 8.47 | 12.9 |
| Jul | 14.2 | 25.0 | 6.8 | 9.3 |
| Aug | 13.7 | 27.2 | 5.33 | 9.3 |
| Sep | 10.7 | 23.9 | 4.48 | 8.1 |
| Oct | 6.3 | 18.2 | 3.82 | 8.6 |
| Nov | 2.4 | 11.5 | 4.82 | 10.3 |
| Dec | -1.6 | 5.6 | 4.76 | 12.3 |

- Mathematical model

  - Description of panel systems

Panel heaters may be installed in three distinctive building elements: floors, walls or ceilings. These elements are brought to a temperature higher than ambient air temperature so that the environment gives off heat by convection and radiation.

At ceiling panels, the main heat transfer mode is radiation, i.e., about 90% of heat is delivered by radiation. Radiation from ceiling heating panels may be very positive to comfort level of the human body. In addition, a significant part of heat is transferred to the surrounding walls and floor, without increasing air temperature . However, one should take into account that too strong radiation adversely affects the thermal comfort of people in the room.

When the thermal comfort is concerned, floor heating is the type of heating that provides a nearly ideal temperature distribution inside a room. Unlike the ceiling panels, floor panels reveal much of the heat by convection (40%). Here, one must take into account the temperature of the floor. There are different recommendations about the values of floor temperature. It ranges between 25 and 28oC. One of the limiting factors of these panels is that they need the free area of thefloor for heating.

Due to limitations in the temperature of the floor and ceiling during floor and ceiling heating, the wall panels obtain  more applications. They are placed on the cold exterior walls, thus prevent the penetration of heat through them. As well as ceiling and floor panels, most of the heat is transferred by radiation, and as opposed to them these panels are suitable for fluids with higher temperatures that results in higher heat flux.

| Figure 2a. Low temperature radiant panel | Figure 2b. Snake pipe in a low temerature radiant panel |
| --- | --- |

  - Primary energy consumption of heating system

The primary energy consumption per heating season of analyzed object was calculated by using the following equation:

(1)

Here,  stands for consumption of natural gas per heating season,  stands for consumption of electrical energy per heating season and R stands for the primary energy consumption coefficient. This coefficient defined as the ratio of total input energy of the energy resources (hydro, coal, oil and natural gas) and the finally produced electric energy. Its value for Serbian energy mix for electrical energy production is R = 3.61 [26].

  - Consumed exergy for heating

The papers concerning low exergy systems (LowEx) by Virtanen and Ala-Juusela [27,28]  encourage the use of low temperature heating systems for buildings. Low exergy heating systems allow the use of low valued energy sources. Such heating systems operate at low temperature levels that are near to room temperature. These systems can provide the occupants with a comfortable, clean and healthy environment. In addition, low temperature systems lead to efficient use of energy and provide flexibility in the choice of the energy source.

The consumed exergy per heating season of analyzed object is calculated by using the following equation:

(2)

here,  stands for consumption of natural gas per heating season, n stands number of heating rooms, To stands for reference temperature,  and stands for inlet and return temperatures of heating emission systems for observed room.

  - Carbon dioxide emission

The total carbon dioxide emission of heating system during a system operation is calculated by using the following equation:

(3)

here,  stands for specific carbon dioxide emission factor of natural gas (kg/GJ),  stands for specific carbon dioxide emission factor of electrical energy (kg/GJ). The emission factors are given in Table 2.

Table 2.The greenhouse gas emission factors for the electric energy and natural gas [29]

| Type of fuel | Emission factor (kg/GJ) |
| --- | --- |
| Natural gas | 206.53 |
| Electric energy | 56.1 |

  - Operating cost

The totally operating costs to run a system are calculated by using the following equation

(6)

here,  stands for the specific cost of consumption of natural gas with energy value of 33338 kJ/m3 (in €/GJ), and  stands for the specific cost of consumption of electrical energy (in €/GJ), k stands for the coefficient of correction quantity of consumed gas k=1.068 [20],  stands fixed monthly cost for meter reading[30]. In this equation we don’t include fixed monthly cost for meter reading of electricity energy because we have more electricity consumer which is a much larger part. The cost factors are given in Table 3.

Table 3.The price of energy in Serbia in May 2011 [29],[30]

| Final energy | Class of consumption | Price |
| --- | --- | --- |
| Electric energy | Green tariff | 0.059 €/kWh |
|  | Blue tariff | 0.089 €/kWh |
|  | Red tariff | 0.177 €/kWh |
| Natural gas | - | 0.41 €/m3 |
|  | fixed monthly cost for meter reading | 0.012 €/month |

- Results and discussion

In this paper, four types of heating systems are simulated. The first system uses floor heating.. The second system is a wall panel heating set at the outer envelope. The third system is the ceiling. The fourth heating system is a combination of floor and ceiling heating. Then, the snake pipe is placed in ceiling and acts as a ceiling heating for the basement room and as a floor heating for the upstairs room. All heating systems use no-condensing natural gas boiler and a circulating pump with continual flow.

  - Results

Simulation results for each of the analyzed panel system are expressed through its energy and exergy consumption, the price of heating (calculated according to current tariffs in Serbia for 2011), and its carbon dioxide emission. Figure 4 shows the consumption of gas, electricity for pumps and primary energy  during heating season. Figure 5 shows  the price of heating. Then, the fluid inlet temperature has the same for all systems at  37oC.

| Figure 4. Energy consumption per heating season | Figure 5. Heating costs per heating season |
| --- | --- |

Figure 6 shows the value of the nominal power of the boiler for all four cases. Figure 7 shows the CO2 emissions per heating season . Figure 8 shows the exergy consumption per heating season.

| Figure 6. Nominal power of boilers | Figure 7. CO2 emission per heating season |
| --- | --- |

Figure 9 shows the obtained values of the mean air temperature of rooms, and the desired temperature of rooms in January. Figure 10 shows the mean temperatures of the surrounding walls and floors in January.

| Figure 8. Exergy for January | Figure 9. The mean and desired temperatures of rooms in January |
| --- | --- |

Figure 10. The mean temperatures of surroundings walls, floors and ceilings during January

Table 4 gives the length of the snake pipe in the panel heating systems . These lengths directly depend of the architecture of the house.

Table 4. The snake pipe length in the panels

| The systems of heating | The pipe snake length in the panels, m |
| --- | --- |
| Floor heating | 1267.19 |
| Wall heating | 1006.59 |
| Ceiling heating | 1068.40 |
| Double side ceiling heating | 633.59 |

  - Discussion

The simulated and obtained parameters are shown in Fig 4-8 for these heating systemsthat operate during the heating period from October 15 to April 15 . It is found that the system 4 has the lowest primary energy consumption (Epry = 8309.81kWh/heating season) and the system 3 has the highest primary energy consumption (Epry =11420.43 kWh / heating season), their difference is about 27%. The System 4 has an primary energy consumption lower by 10% compared to the System 2, and lower 22% compared to the system 1. The electricity slightly affects the overall energy required and the lowest electricity consumption is in the case with the system 4 (22.96 kWh/heating season), and highest electricity consumption in the system 3 (37.13 kWh/heating season).Figure 5 shows that the largest cost is that of the heating system 3 (624.02 euro), and the lowest that of the heating system 1 (475.58 euro). The use of the system 1 instead of the system 3 means a total financial savings of 148.33 euro per heating season. The minimum nominal power of the boiler is required for the system 4 (9885 kW), and the highest for the system 3 (15988 kW). The nominal power outputs by the other two systems are similar as by the system 3. The CO2 emissions  is the highest by the system 3 (Ssys kgCO2 = 2847.57), and the lowest by the system 4 (Ssys kgCO2 = 2068.29). Figure 8 shows the consumed exergy in January when temperatures are the lowest. Then, the exergy is the smallest by the system 4 (87.50 MJ), and highest by the system 3 (114.68 MJ).

To check proper operation of all four systems, Figure 9  shows the mean internal air temperature in relation to the temperature set by thermostats. It is found that in all heating systems, the mean internal air temperatures do not significantly deviate from the desired temperature, due to the heat gains from of the neighborhood rooms  and the direct radiation from the low-temperature panels. The largest deviation occurs in the heating system 4 in the room SS3. The value of this deviation is about 5% (1.1oK), so that the mean temperature in this room is 18.0°C instead of the desired 20°C  . To monitor the appearance of unsolicited overheating and too cold walls, Figure 10 shows the mean temperatures of surrounding exterior surfaces. All temperatures are in the range between 17.5 and 27 oC, but the temperature jump is a phenomenon characteristic for the wall where the low temperature panel is integrated.

The length of snake pipe embedded in the panels is the lowest for the heating system 4 (633.59 m1), and the highest for the heating system 1 (1267.19 m1), which makes a difference of about 50%. This length depends directly on the architecture of the building and the size of the panel.

- Conclusions

This paper analyzes the four low-temperature radiant panel systems: floor heating, wall heating, and ceiling heating and ceiling-floor  heating. the classic no condensing natural gas boiler is used as a source of energy. The boiler is  connected to a circulation pump with constant flow. The family house for the city of Kragujevac is analyzed with architecture developed within the project "Development of a net-zero-energy house." The operating of each heating system is evaluated through the consumption of primary energy, operating cost, and emissions of pollutants.

It is found that the double-sided ceiling heating system has the lowest energy, exergy, CO2 emissions, operating costs , and the nominal power of the boiler. The worst system by all these parameters is the classical ceiling heating. Also, it is important to note that the next better system is the system 2 (heating panel).

The comparison of the room air temperatures and the desired temperatures, shows that all systems give satisfactory results without significant deviations. The largest deviation is  found with two-sided ceiling panel system 4 and the temperature in this room is 18.9oC. However, it have in mind that the using of the radiation heaters may achieve thermal comfort with up to 2°C lower temperature of internal air than that required by the standard. The surrounding exterior surfaces have the lowest temperature at 17.5 degrees that occurs in the case of double-sided ceiling panel system 4 in room SS3 at the first floor. The temperature occurs at its adjacent outer surfaces without any embedded heating panels.

It should noted, that the two-sided ceiling panels require the lowest length of snake pipes in the panels and the wall panels need the highest length of snake pipes. .

Because of the applicability of the low-temperature heat sources (heat pumps, solar energy, geothermal energy), in these systems used heating water of the inlet temperature of 37oC.

Acknowledgment

This paper is a result of two investigations: (1) project TR33015 of Technological Development of Republic of Serbia, and (2) project III 42006 of Integral and Interdisciplinary investigations of Republic of Serbia. The first project is titled “Investigation and development of Serbian zero-net energy house”, and the second project is titled “Investigation and development of energy and ecological highly effective systems of poly-generation based on renewable energy sources. We would like to thank to the Ministry of Education and Science of Republic of Serbia for their financial support during these investigations.

References

[1] Kilkis BI, Sager SS, Uludag M. A simpliIed model for radiant heating and cooling panels. Simulation Practice and Theory 1994;2:61–76;

[2] Lisa LM. Radiant heating provides energy-e-cient versatility. Professional builder and remodeler. 1992.

[3] Stetiu C. Energy and peak power potential of radiant cooling systems in US commercial buildings. Energy and Buildings 1999;30: 127–38.

[4] Yost PA, Barbour CE, Watson R. An evaluation of thermal comfort and energy consumption for a surface mounted ceiling radiant panel heating system. ASHRAE Transactions 1995;101(1):1221–35.

[5] Simmonds P. Practical applications of radiant heating and cooling to maintain comfort conditions. ASHRAE Transactions 1996;102(1):659–65.

[6] Simmonds P. Control strategies for combined heating and cooling radiant systems. ASHRAE Transactions 1994;100(1):1031–9.

[7] Olesen BW. Comparative experimental study of performance of radiant 6oor heating systems and a wall panel heating system under dynamic conditions. ASHRAE Transactions 1994;100(1): 1011–23.

[8] Gibbs DR. Control of multi-zone hydronic radiant 6oor heating systems. ASHRAE Transactions 1993;99(1):1003–10.

[9] Leigh SB, MacCluer CR. A comparative study of proportional 6ux-modulation and various types of temperature-modulation approaches for radiant 6oor heating system control. ASHRAE Transactions 1994;100(1):1040–52.

[10] MacCluer CR. The response radiant heating systems controlled by outdoor reset with feedback. ASHRAE Transactions 1991;97(2): 795–9.

[11] Kollmar A, Liese W. Die strahlungsheizung, 4th ed. Munchen: R. Oldenbourg; 1957.

[12] Leal RLV, Miller PL. An analysis of the transient temperature distribution in pavement heating installations. ASHRAE Transactions 1972;78(2):71–8.

[13] Zhang Z, Pate MB. A numerical study of heat transfer in a hydronic radiant ceiling panel. In: Chen JLS, Vafai K, editors. Numerical methods in heat transfer, vol. 62. New York: ASME-HTD: 1986.

[14] Zhang Z, Pate MB. A semi-analytical formulation of heat transfer from structures with embedded tubes. In: Kuehn TH, editor. Heat transfer in buildings and structures, vol. 78. New York: ASME-HTD: 1987. p. 17–25.

[15] Kilkis BI, Eltez M, Sager S. A simpliIed model for the design of radiant in-slab heating panels. ASHRAE Transactions 1995;99(2):210–6.

[16] Kilkis BI, Sapci M. Computer-aided design of radiant sub-floor heating systems. ASHRAE Transactions 1995;99(2):1214–20.

[17] Kilkis BI, Coley M. Development of a complete software for hydronic 6oor heating of buildings. ASHRAE Transactions 1995;99(2):1201–13.

[18] Maloney DM, Pederson CO, Witte MJ. Development of a radiant heating system model for BLAST. ASHRAE Transactions 1988;94(1):1795–808.

[19] Strand RK, Pederson CO. Implementation of a radiant heating and cooling model into an integrated building energy analysis program. ASHRAE Transactions 1997;103(1):949–58.

[20] Strand RK, Pederson CO. Modeling radiant systems in an integrated heat balance based energy simulation program. ASHRAE Transactions 2002;108(2):1–9.

[21] Miriel J, Fermanel F, Mare T. Modeling of water ceiling radiant panel heating and cooling system—interaction between air velocity and temperature Ields. Computational technologies for 6uid/thermal/structural/chemical systems with industrial applications. ASME; vol. 1. 1999. p. 285–91.

[22] Abdelaziz Laouadi. Development of a radiant heating and cooling model for building energy simulation software Building and Environment 39 (2004) 421 – 431

[23] Meteonorm,Global Meteorological Database for Engineers, Planners and Education: http://www.meteonorm.com, Retrieved May 2011

[24 M.Bogner, M. (2002). Technical regulations about heating, cooling and air conditioning (in Serbian). Belgrade: SMEITS.

[25] World Meteorogical Organization: http://worldweather.wmo.int/101/c00198.htm Retrieved May 5, 2011,

[26]http://www.ssllink.com/mre/cms/mestoZaUploadFajlove/ENERGETSKI_BILANS_PLAN_ZA_2008, Retrieved May 5, 2011.

[27] M. Virtanen, M. Ala-Juusela, Increased energy efficiency and improved comfort, Paper No. 1494, 9th REHVA World Congress- Clima 2007, 10–14 June, Helsinki, Finland.

[28] M. Ala-Juusela, Heating and Cooling with Focus on Increased Energy Efficiency and Improved Comfort, Guidebook to IEA ECBCS, Annex 37, Low Exergy Systems for Heating and Cooling of Buildings, VTT Technical Research Centre of Finland, 2003

[29] Interklima: http://www.interklima.rs/03_01cena_pg.html, Retrieved May 5, 2011

[30] Interklima: http://www.interklima.rs/01_14nacin_obracuna.html, Retrieved May 5, 2011